## Slide 1: INNOVATIVE APPROACHES FOR PEAK FLOW REDUCTION IN NORTH HUDSON’S COMBINED SEWER NETWORK
CSO Permittee Network Meeting
April 19, 2019
Mott MacDonald, Iselin, NJ
Kevin Wynn, PE
Karen Karvazy, PE
Notes: KK

## Slide 2: Presentation Outline
NHSA Background
Stormwater Management Tool
Use of Automated Valves
Program Observations
The Path Ahead

## Slide 3: Background
North Hudson Sewerage Authority
    City of Hoboken
    Weehawken,
    West New York,
    Union City
Notes: North Hudson Sewerage Authority owns and operates the sewerage system for four municipalities. Across is Hudson River and New York City.

## Slide 4: Background - Topography

## Slide 5: Background
Notes: Need to make more clear municipality names (Hoboken, West New York,
Need to note

## Slide 6: Background
Authority Sewer Connection Review Process
  Any change in development is reviewed by the Authority
    Review of stormwater management report
    Review of Engineering Plans
    Redevelopment
    Impervious Coverage
Chart: Sewer Connection Reviews
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Number of Applicants | 31 | 31 | 28 | 53 | 67 | 74 | 44 | 57
Notes: Give an I dea of something else which is in the NHSAs favor which is stormwater discharge control from new sites.

## Slide 7: North Hudson Sewerage Authority Stormwater Control
NHSA Stormwater Control Design Guidelines: 2000-2017:
  Loosely planned guidelines , development requirements of the New Jersey Administrative Code:
  “Design stormwater management measures so that the post-construction peak runoff rates for the 2,10 and 100-year storm events are 50, 75 and 80 percent, respectively, of the pre-construction peak runoff rates.”
  Applications to NHSA showed large variability in modeling method, calculations in existing Impervious Area.
  What does this do for meeting the Authority’s Long Term Control Goals?
c
Notes: Submittal of a Stormwater Report – Show Existing Conditions Proposed Conditions Choose modelling method between modified rational, rational, etc.
Good for design of large scale stormwater controls.
Need a process to address smaller events (Return Period<=2year).
NHSA targeting to address <1 acre sites that do not trigger the State stormwater requirements.
Plan is to reduce hydraulic load on ageing and undersized sewer system.
Small and more frequent events lead to CSO overflows.

## Slide 8: The Tool
    Background optimizer algorithms – Microsoft Visual Basic for Applications (VBA IDE) platform.
    Object Oriented Programming – “objects” in Excel.
    Available as part of MS Office Suite (Word, Excel, Access etc.).
    Worksheet – Excel functions.
VBA Script

## Slide 9: The Tool
c
Interpretation
    TR-55, Woods in Good Condition
    Trees and Rocks
    Impervious Area: Run-off Curve Numbers for Urban Areas: 98
    Reduce to run-off curve number of Wooded Conditions: 70
    Basis: 2-year , 24-hour storm (3.3 inches)

## Slide 10: The Tool
Notes: David – I don’t know if I can use this slide – this is a video. really only want to see the part that shows the reporting tool
So – that would be the end of the story – except there were issues now in with the implementation . Leads us to the use of automated controls within the collection system

## Slide 11: Program Implementation
Program Challenges
    Small sites (under 0.3 acres) require a minimum orifice size to prevent clogging, but allows too much flow for peak shaving.
    Limits to passively controlled systems – only use gravity, but need certain size orifice, but cannot hold back flow in system.
Program Assists
    3 of 4 Municipalities have passed the Inspection Program.
      Allows Inspections on Private Property
      Corrective actions for failure to maintain system

## Slide 12: Use of Automated Control Valves
    All Sites > 10,000 square feet are required to install automated valves to control stormwater.
      OPTI Valves – real time control
      Mission Communications – NHSA Operated Valves
    New requirements for Owner-Authority Access Agreements
      Reviewed During the Sewer Connection Application Phase
      Recorded with Hudson County Property records

## Slide 13: CMAC Technology
Secure continuous monitoring and adaptive control
  Built on modern cloud architecture
  Web-based dashboards
  Provides data transparency and infrastructure intelligence
  Applies where timing, duration, volume, and peak flow reduction are important.
CMAC Technology
Notes: MS:

## Slide 14: Projects – Southwest Park
Southwest Park, Hoboken, NJ
67,000 gal total capture
0.88 acre watershed
Can retain half of volume to release in dry weather
Notes: MS:

## Slide 15: Projects – Southwest Park
Southwest Park, Hoboken, NJ
Notes: MS

## Slide 16: CMAC Technology
CMAC Technology
Simulated Passive System
Observed CMAC System
Sim
SIMULATED PASSIVE SYSTEM
OBSERVED OPTI SYSTEM
Notes: MS

## Slide 17: Projects – Monroe Center
Monroe Center, Hoboken, NJ
Notes: MS:14 story high-rise PP v

## Slide 18: Automated Control Valves
  In Service
  Southwest Park – Hoboken
  Under Construction
  Monroe Center
  In Planning
  PSE&G Substation - Hoboken
  Carrigan Avenue – Union City
  1300 Manhattan Avenue
Notes: KK

## Slide 19: Program Observations
  Sewer Use Resolution Passed October 2018. Since Implementation:
  There is streamlined stormwater review process.
    Developers are using Green Infrastructure to meet our Program Goals.
      Permeable Pavement
      Green Roof
c
Notes: KK

## Slide 20: Conclusions
  These efforts will contribute to goals in LTCP:
  NHSA is implementing the Stormwater Management System Inspection Program.
  The Online Tool is dynamic, NHSA can update it as the program evolves.
  Continuation of Long Term Program – a new feature in the NHSA’s CSO tool box.
Notes: KK

## Slide 21: Special thanks to: Fredric J. Pocci, PE North Hudson Sewerage Authority Don Conger, Project Director, Jacobs
Kevin Wynn, PE kevin.wynn@mottmac.com
Questions?